## Slide 1: Plato optimization-based design
Plato Software Development Team
Trilinos User Group Meeting
November 1st, 2023

## Slide 2: Plato: optimization-based geometry design
Sierra Mechanics
Gradient-Based Optimization
Shape
Topology
Mesh
Strategy for automated design:
Quantify quality of design via simulation
Formulate a mathematical optimization problem.
What Plato allows users to do:
Orchestrate the workflow
Use gradient-based methods
Automatically compose function evaluations across software packages for
  Geometry
  Meshing
  Physics Simulation
Plato’s purpose at Sandia:
Platform for shape/topology optimization
Platform for continued research
Bread & butter: compliance min., stress-constrained mass min., mass mocks

## Slide 3: Plato: FY23 Q3 Noteworthy Items
  HOW ARE YOU DELIVERING ON 1IC?
    Production-ready thrust – improved build/test process integrated with Sierra, partnership with analysts
    Incorporation of ROL’s stochastic optimization capabilities via V&V project
    Ability to work with and connect to Sierra Mechanics
    Plans to leverage 1540 UX/UI experience/capabilities
  PERFORMANCE TO PLAN HIGHLIGHTS:
    Removal of Plato’s legacy optimizers completed. This offers access to new algorithms and reduces our code maintenance burden through removal of 64k+ lines of code!
    Joshua Robbins putting together EDC demonstrator for mass property shape optimization based on SD Modal tool functionality
    Full continuous integration with merge gating enabled for Plato! Easier to use Sierra with Plato and substantially improves Plato’s code credibility moving forward.
Removal of legacy Plato
Optimizer and
full use of ROL
Has resulted in these advantages:
Removed 64K lines of code & technical debt!
Reduced maintenance burden
Increased code sharing
ROL is only gradient-based optimizer available in Plato
With help of DevOps, Plato is now on SRN under Continuous Integration
Has resulted in these advantages:
More secure development
Closer integration with Sierra
Closer integration with FuSED
Vastly improve code quality
Always in a releasable state
Over 64K lines of code deleted!
+

## Slide 4: Hook up Tacho Solver
Customer: ASC/Plato
Purpose:
Epic Goal: Enable Plato Analyze use of ShyLU_Node solver Tacho
Sprint Goal: Plato interface is completed, Tacho is solving problems
Impact:
High-performance cross-platform shared-memory linear solver available in Plato
More robust testing, CPU-based testing
Performance improvements?
Notes: Sean

## Slide 5: Hook up Tacho Solver
Instead of a few days’ effort, this turned into a two-sprint odyssey.
Thanks for your help:
Clark Dohrmann – lending us his interface
Kyungjoo Kim – helping us compile it
Christian Trott – helped us update to newer version of Kokkos
Notes: Sean

## Slide 6: Hook up Tacho Solver
Timing comparison with AmgX (@ 1e-12) on compliance minimization problem
DOFs | Tacho runtime (forward solve) | AmgX runtime (forward solve) | Tacho runtime (optimization) | AmgX runtime (optimization)
10245 | 14 s | 15 s | 11 s | 18 s
86559 | 12 s | 16 s | 29 s | 35 s
195357 | 14 s | 16 s | 53 s | 91 s
626409 | 36 s | 19 s | 170 s | 136 s
931500 | 50 s (14 GB mem) | 22 s | 252 s | 191 s
1470714 | Out of memory | 26 s | Out of memory | 300 s
4857837 | Out of memory | Out of memory | Out of memory | Out of memory
Notes: Sean

## Slide 7: Hook up Tacho Solver
Large startup cost obscures behavior for small problem sizes
AmgX scales better for large problems, as expected
GPU build of Tacho limited by 32-bit integer indices (this is a choice), device memory.
Tacho amortizes symbolic factorization cost significantly: subsequent solves in optimization loop much quicker than the first
To try:
  Tacho multi-core CPU builds on larger systems (no device memory limit)
  Tacho with higher-order elements (AmgX struggles)
Notes: Sean

## Slide 8: Hook up Tacho Solver
Timing comparison with AmgX (@ 1e-12) on orthotropic compliance minimization problem (poorly conditioned linear system)
DOFs | Tacho runtime (optimization) | AmgX runtime (optimization)
32448 | 21 s | 102 s
Summary
Tacho is faster for up to a few hundred thousand DOFs
Tacho is faster and more robust for poorly-conditioned systems
Tacho works on CPUs and non-nVidia hardware
We will default to Tacho but keep AmgX
We will delete our interface to Epetra-based solvers
Notes: Sean

## Slide 9: Mass mock design
Target
Topology Optimization
Additive Manufacturing
Machining
CAD
Shape Optimization
EDC Demonstrator
Topology Optimization
Rapid interrogation of target properties
Material downselect
Inspiration
Shape Optimization
Dialing it in
EDC demonstrator
shape optimization of mass properties
web-based UI components
SGM

## Slide 10: Long-term Vision for Matching Dynamics (FY24+)
User-friendly tools for mass/dynamic mock design and fixture design that drive development of UI/UX components and connection to DEE.
Automatic conversion of CAD to simplified CSG (SGM)
Mass-properties-aware simplification
Improved numerical algorithms (Sierra/SD)
Shape sensitivity for shells and contact; investigate MPE sensitivity
Great opportunity to refactor and clean up Plato-SD interface
Improved problem formulation (FuSED/ROL)
Optimal selection of measurement locations
Generalization measurement operators to account for experimental data.
Level-set Methods for Topology Optimization (LDRDs: Alberdi, Dugger)
Necessary to get good solutions with dynamic physics

## Slide 11: Mass Mock Modal Matching
Modes measured at blue dots on the bottom of the geometry
Notes: Ryan

## Slide 12: Mass Mock Modal Matching
Initial
Gold
Notes: Ryan

## Slide 13: Modal assurance criterion (mac)
Notes: Ryan

## Slide 14: Mass Mock Modal Matching
Gold | Optimized
2.5 | 2.522263
2.5 | 2.506502
5 | 4.997805
1.5 | 1.519576
4.25 | 4.315312
4 | 4.255144
3.75 | 3.547251
3 | 2.966192
7 | 7.199514
Notes: Ryan

## Slide 15: Modal assurance criterion (mac)
Notes: Ryan

## Slide 16: Mass Mock Modal Matching
Initial
Gold
Notes: Ryan

## Slide 17: Modal assurance criterion (mac)
Notes: Ryan

## Slide 18: Mass Mock Modal Matching
Optimized
Gold
Notes: Ryan

## Slide 19: Modal assurance criterion (mac)
Notes: Ryan

## Slide 20: Parallelization of Stochastic ROL
Customer: ASC
Purpose:
Epic Goal: Integrate stochastic ROL methods
Sprint Goal: Implement parallelization
  Stochastic methods evaluate large numbers of samples
  Batch compute objectives/gradients over available physics codes
Future work:
  Write report
Impact:
Running stochastic problems is more practical
Gaussian distribution load
32 samples

## Slide 21: V&V Project Final Report
Customer: ASC
Purpose:
Epic Goal: Integrate stochastic ROL methods
Sprint Goal: Write final V&V report
  Summarized work completed and implementation details
  Demonstrated parallel speed-up
  Provided examples of larger scale problems
Impact:
Reporting and documentation of stochastic optimization features
Risk neutral
Risk averse

## Slide 22: Bracket Optimization
Purpose:
Sprint Goal:
  Validate bracket designs
  Follow-up optimization
  Stress constrained mass minimization
Results:
Provided several optimized designs for different stress constraints
Customer to additively manufacture in 316 stainless
Design volume
Notes: Sean

## Slide 23: 316 Stainless Steel
Stress constraint: 50.4 ksi
Volume: 23.6 in3
Mass: 6.7 lbs
Vol frac: 15.2%
Original volume: 155.2 in3
Original mass: 44.5 lbs

## Slide 24: Analysis Results
Extract surfaces from results
Remesh with tets
Run in Sierra/SD with a mounting bracket to mimic trailing arm and tet10 elements
Tied contact BC for weld at interface of the two blocks
Fixed BCs placed on back of bracket
Fixed

## Slide 25: 316 Stainless Design
Von Mises stress, capped at 52 ksi
Yield strength 59 ksi
Center cut-through
Max Von Mises stress >300 ksi

## Slide 26: Modified fixed BCs
Stress constraint: 50.4 ksi
Volume: 35.5 in3
Mass: 10.2 lbs
Vol frac: 22.8%
Original volume: 155.2 in3
Original mass: 44.5 lbs
Fixed tangential displacement components
Free normal components

## Slide 27: Modified fixed BCs
Von Mises stress, capped at 52 ksi
Center cut-through

## Slide 28
316 stainless steel
Stress constraint: 60% yield strength (35.6 ksi)
Mass: 12.7 lbs
Stress constraint: 70% yield strength (41.5 ksi)
Mass: 10.3 lbs
Stress constraint: 80% yield strength (47.5 ksi)
Mass: 8.7 lbs

## Slide 29: conclusion: Direction of plato
Plato has an entrepreneurial history…
Focus on research capabilities: proof of concept without maturation
Development of its own optimizers, physics code
Success in proving capability, bringing in SPP, LDRD funding
but now is becoming a production code:
Strengthening Agile practices
Incorporation of Continuous Integration (CI)
Switch to ROL, pivot focus to Sierra Mechanics while maintaining AM engagements
Desired relationship with Trilinos:
Strong collaboration with ROL on research, optimizer development, stochastic problems
Continued engagement with Kokkos for performance portability
Development of Tacho: need for performance-portable shared-memory sparse-direct linear solver